## Slide 1: EE 101 Final Project
By: Kyle Werner, Jack Thomae, Carlo Giorelli, Gepy Bernstein

## Slide 2: Homemade Color Sensor
Board of provided color sensor became inoperable, as we read consistent, erroneous values
Used a small breadboard, photocell, multi-color LED, and potentiometer
Worked as expected and with correct values

## Slide 3: New Robot Body
Decided to replace plastic robot body parts with cardboard
Allowed freedom to place sensors in optimal locations
Slight weight advantage

## Slide 4: The Code
Heavily reliant on structured programming
Arrays simplified functions and were used for many variables (ex. Input pins, colors on the color sensor, etc.)
Created functions for all of the sensors and motors and what they would be needed for
Created “states” that combined the required functions for each of the objectives (find the maze, go through the maze, find the blue block, push the blue block out, return to the arena)
Used Boolean flags to check if all objectives were met

## Slide 5: Example Code
void Maze() {
bool FoundWall = false;
if((FoundWall && checkUS(2) > 35)){
drive(50, 25);
delay(200);
}else if (checkUS(0) <= 25) {
drive(50, 25);
delay(200);
}else if (checkUS(2) <= 35) {
drive(50, 50);
delay(200);
}else {
drive(50, 50);
delay(200);
}
}
Code used for traversing maze
Drive operates the motors and maps analog values to values for 0-100 (percent of motor speed)
  Bias allows the robot to turn left or right
checkUS is a function that reads the distances (in cm) of the closest object of the three mounted ultrasonic sensors
  0 is the front sensor, 1 for left, 2 for right